## Slide 1: Costs and benefits of forest restoration - ecological, social, and economic
Prasit Wangpakapattanawong

## Slide 2
Outline
Cost
    Time
    Financial
Benefits
    Products
    Water services
    Carbon sinks
    Biodiversity conservation
    Opportunities for ecotourism
Production, management, restoration, collaboration

## Slide 3
Conception/management – meetings
Administration – regulation, dispute resolution, reporting, accounting, benefit sharing
Training
Cost-Time

## Slide 4
Legal/admin fees
Survey costs – baseline carbon, timber and NTFP’s
Forest maintenance/ management – paid labour or voluntary?
Particularly FIRE PREVENTION
Cost-Financial

## Slide 5
Production Value Foregone
1.94 $ per Kg

## Slide 6
Production Value Foregone
S. Thailand – current income from oil palm about 600 US$/ha/y from 7 to 15 years after plantation establishment.
951.25$ per metric ton

## Slide 7
Restoration cost
Measures the density and species richness of natural regeneration and identifies factors impeding its progress
Pre-planting rapid site assessment
Collaborative Costing

## Slide 8
Restoration cost
Pre-planting survey
Site preparation
Tree planting
Weeding/fertilizer
Monitoring for two years
Fire prevention for two years
Livestock exclusion
Reporting / accounting
The costs of forest restoration depends on location
The degree of degradation
Distance to restoration site
Local daily labor rate (9.5$ per day in Chiang Mai)

## Slide 9
Restoration costs
Example
Local cost parameters
THB
1. Survey, estimated no. of existing natural regenerant per ha 1000 per ha
Therefore, the recommended number of tree to plant is 2086 per ha
2. Distance from nursery to restoration site & return 30 km
Distance from homebase to restoration site & return 30 km
Current price of liter of fuel 35 THB
Enter the average fuel efficiency of vehicles to be used in km/liter 12 km/l
3. Daily labor rate 346 THB
Salary of project staff/supervisor 18,000 THB
Total area to be restored 20 ha
Enter the annual inflation rate (forecast for next 2 years) 3% /y
???

## Slide 10
Restoration costs
=170,569 THB

## Slide 11
1.29 US$/TREE
0.58 US$/TREE
Restoration costs
Daily labour 10 US$/day
Site survey and planning
Trees and planting
Weeding and fertilizer application for 2 years + fire prevention.

## Slide 12
Benefits
    Products
    Water services
    Carbon sinks
    Biodiversity conservation
    Opportunities for ecotourism

## Slide 13
Non-Timber Forest Product (NTFP)
Compared with NATURAL RUBBER
13.1 billion US$ (2018)
-22.1% drop in value since 2014 when natural rubber shipments were worth $16.8 billion. Year over year, exported natural rubber depreciated by -19.9% from 2017 to 2018
At least 150 different forest products, including rattan, bamboo, nuts, essential oils and pharmaceuticals, traded internationally, contribute about US$ 4.7 billion/year to the global economy.

## Slide 14
But NTFP trade requires
Sustainable management, by monitoring and research
Appropriate land tenure, taxation and legislative systems
Access to global markets – promotion advertising
Integration of traditional knowledge into NTFP research and management
Non-Timber Forest Product (NTFP)

## Slide 15
Some forest-dwelling people depend on forest products for subsistence – but the numbers are probably declining.
More often, gathering or selling such products provides a safety net for the rural poor when times are bad
Non-Timber Forest Products (NTFPs)
Value is quantified as “replacement” costs

## Slide 16
Measure standing crop and growth rate
Annual harvest must be < annual production
Calculate quotas
Issue permits
Record total harvest (weight) and harvest “effort” (usually time).
Enforcement – dealing with transgressors
Cost of administration > income from product?
Achieving Sustainable Harvesting

## Slide 17
Trend is often towards species domestication – which can provide an incentive to deforest
Exception – mycorrhizal fungi which grow associated with forest trees
Achieving Sustainable Harvesting
Danger in relying on NTFP’s as forest “value”

## Slide 18
Subsistence products
GDP
Traded products
Replacement products
GDP rise
=> economic growth
GDP rise
=> Recession
Sell logs
Pay wages
But are we really richer?

## Slide 19
Productive forest
Degraded forest
NTFP’s
Water
Carbon storage
Biodiversity
Few usable products
Soil erosion
Global warming
Species loss

## Slide 20
What about local people?
GDP rises but they are poorer
GDP rise

## Slide 21
Forest destruction always results in net economic loss at the national and local levels.
By measuring prosperity by GDP, we don’t value all the benefits of forests.
So should governments invest in forest restoration?
https://www.xinhuathai.com/china/147021_20201020

## Slide 22
Watershed Services
Deforestation increases water yield, but outflow becomes more seasonal.
Tropical forests add enormous quantities of organic matter to soils, which increases their field capacity
Such soils soak up water during the rainy season (reducing floods) and release it gradually during the dry season (reducing droughts).

## Slide 23
Watershed Services
Deforestation exposes the soil to erosion and compaction. Absorptive top soil is rapidly lost. Infiltration is reduced and runoff increases, resulting in flash floods & landslides

## Slide 25
Watershed Services
Flow is lower but more constant in all seasons. Sedimentation low.
Flow is higher in rainy season. High sedimentation begins to reduce river channel volume.

## Slide 26
Increased runoff + reduced river channel volume
= Flash floods

## Slide 27
Thailand Floods 2011: 815 deaths and 42 billion US$ damage to infrastructure and industry. The 7th costliest disaster in human history.

## Slide 28
How to monetarize watershed services?
https://www.researchgate.net/publication/40110859_Pay_-_Establishing_Payments_for_Watershed_Services
Linking land and water use to downstream benefits
Valuation of watershed services

## Slide 31
Carbon sink
Tropical forests absorb more CO2 than they emit about 1.3 gigatonnes* of carbon (GtC) per year (Lewis et al., 2009)
Lewis, L. S., et al., 2009. Increasing carbon storage in intact African tropical forests. Nature, 457: 1003-1007
= 16.6% of carbon emissions from burning fossil fuels and the cement industry
= 60% of the sink provided by all of the terrestrial vegetation on Earth.

## Slide 32
Carbon sink
“ … natural forests are 6 times better than agroforestry and 40 times better tan plantations at storing carbon (sequestering 12, 1.9 and 0.3 Pg C per 100 Mha by 2100, respectively).”
Lewis, L, C. Wheeler, E. Mitchard & A. Koch, 2019. Restoring natural forests is the best way to remove atmospheric carbon. Nature 568: 25-28

## Slide 33
Carbon sink

## Slide 34
Carbon sink
Tropical forests store about 240 tC/ha in trees/soil.
Crop lands - 80 tC/ha mostly in soil.
Clearing 1 ha of tropical forest emits about 160 tC & also reduces subsequent sequestration rate.
Agriculture also releases methane, which is 20 times more efficient at trapping heat than CO2 is.
240 tC/ha
80 tC/ha

## Slide 35
How to monetarize carbon – carbon credits

## Slide 37
Type of Carbon Credits
Compliance credits (CER’s) – governments and corporations legally obliged to buy credits to meet targets set by national laws.
Voluntary Credits (CCX’s or CRT’s) – individuals or organizations taking responsibility for their own carbon footprints.

## Slide 38
Type of Carbon Credits
http://www.climatechange.lk/DNA/carbon_market.html

## Slide 39
Carbon credits are traded on international markets. Prices fluctuate a lot! But unlike rubber and palm oil, the recent trend is UP.

## Slide 40
Restoration by framework species method: carbon in trees goes back to normal levels in about 16 years

## Slide 41
Using The framework species method, profits from carbon sequestration over 14 years ranged in NPV from 22,215.45 to 25,157.04 US$/ha.
Profits from maize cultivation (a major regional deforestation driver) averaged just 1,347.53 US$/ha over 14 years,
Jantawong, et al. 2022. Financial Analysis of Potential Carbon Value over 14 Years of Forest Restoration by the Framework Species Method. Forests 2022, 13, 144. https://doi.org/10.3390/f13020144

## Slide 42
REDD policy
Policies and incentives under the UN Framework Convention on Climate Change to reduce CO2 emissions from clearing/burning forests.
REDD = Reducing Emissions from Deforestation & Degradation
It is paying people NOT to cut or burn forests but People who had no intention of clearing forest, may start deforestation to get payments.

## Slide 43
REDD policy
“…enhancement of carbon stocks …” COP15 2009 4CP/15.
REDD to REDD++
Include forest restoration to absorb CO2 by tree planting or assisting natural regeneration
Include “full and effective engagement of indigenous people and local communities …”
Include “… consistent with conservation of natural forests and biodiversity …”

## Slide 44
Biodiversity
Pollinators support agriculture
Biodiversity
NTFP diversity
economic adaptability
security

## Slide 45
Biodiversity
Wildlife tourism
    1-day Bird Tour Khao Yai: 66 – 237 US$/day
http://www.wildbirdeco.net/photo-review/birding-tour/item/431-bird-watching-in-khao-yai-np-thailand.html

## Slide 46
Chart: 
| WATERSHED SERVICES | CLIMATE REGULATION | GENETIC RESOURCES | RAW MATERIALS | TOURISM | AIR QUALITY | MEDICAL | FOODS
 | 2374 | 1965 | 483 | 431 | 381 | 230 | 181 | 75
Potential value of ecosystem products/services from 1 ha of tropical forest (US$/y)
S. Thailand – current income from oil palm about 600 US$/ha/y
TOTAL = 6,120 US$/ha/y
The Economics of Ecosystems and Biodiversity (TEEB) study. www.teebweb.org
DIVERSITY REDUCES RISK
Thank you for your attention.
Please also visit forru.org